## Slide 1: Root Cause and corrective action (RCCA)
MPIA Quality Alliance 2023 Webinar Series
Presenter: Daniel Juliano
Director, Montana State University Technology Transfer Office
Notes: Hello! Welcome to the MPIA Quality Alliance webinar series. The MPIA Quality Alliance is a sub-committee of the Montana Photonics Industry Alliance in Bozeman, Montana. Our mission is to provide helpful tools for implementing Quality Management Systems. This presentation is one of series of recorded presentations and webinars designed to assist organizations with implementing quality processes as solutions to common manufacturing problems.
My name is Daniel Juliano. I am the Director of the Technology Transfer Office at Montana State University.
This presentation provides a template for implementing an RCCA Process in your organization. It’s a powerful tool both in the context of implementing a Quality Management System or in solving almost any difficult problem.

## Slide 2: Agenda: This is what you will learn
What is Root Cause and Corrective Action (RCCA)?
Why implement RCCA?
How do I implement RCCA?
How will RCCA improve the organization?

## Slide 3: What is RCCA?
RCCA process is a methodical, effective, and efficient structured problem solving approach
Goal: solve each problem only once
RCCA core:
  Find problem root cause
  Apply containment (short-term solution)
  Implement corrective action (long-term solution that prevents recurrence)
Notes: Best case is to avoid ever having a given problem. Obviously should do that whenever possible.
Next best is to solve each problem once and never see it again. That is an example of continuous improvement.
Worst is to fight the same fires repeatedly—an avoidable and unnecessary waste of scarce resources.

## Slide 4: Why Implement RCCA?
Do the same problems seem to occur repeatedly?
Do you have the sense that you are wasting resources on “Band-Aids” that steadily accumulate and
  degrade your ability to deliver quality products on time?
  burden engineering with an increasing number of urgent design revisions?
  are making your operation more difficult to manage over time instead of easier?
Is it unclear who is responsible for solving a given problem, once identified?
Is it often unclear whether or not a problem has really been solved?
Implementing RCCA will avoid these problems
Notes: If the answer to one or more of these problem is YES, then a structured RCCA process is likely to be helpful at your company.

## Slide 5: Sample use cases for RCCA
Quality: Customer returned a failed laser after <1 month of use
Engineering: Pushing limits of production equipment speed causing failure of the equipment
Safety: Employee slipped on wet sticky mat and was injured
RCCA useful in diverse contexts
Notes: The typical use case for RCCA is to solve a quality problem i.e. an excursion from the expected and desired state. But you can also use the RCCA technique to apply to many other situations, including solving difficult engineering problems or addressing safety issues.
It may be easier to understand the RCCA process using some concrete examples. In the following slides, I will use the 3 examples on this slide to illustrate how the process works.

## Slide 6: How to implement RCCA –7 elements
Title & RCCA #
Executive Summary
Containment
Root Cause Analysis
Corrective Action
Action Item List
Signoff
7 elements to this RCCA template—
all critical to the effectiveness of the process
Notes: The following 7 slides provide an RCCA template, designed to be used to step through the RCCA elements during a review meeting. Many variations of this template exist online. This version of RCCA is simplified and customized to make it as efficient as possible, with minimum jargon and maximum impact. Give it a try, and feel free to modify it to suit your particular situation.

## Slide 7: RCCA #
Title:
Date:
Owner:
Notes: RCCA # because all RCCA’s should be tracked somewhere—spreadsheet, database, Sharepoint, MS Teams, etc. to ensure they are driven to closure and for future reference. This is a form of traceability.
Owner is key for accountability. Owner might change over time e.g. after root cause analysis is completed.

## Slide 8: Executive Summary
Problem Statement
What was the impact and why do we care about it?
Current Status
Notes: Problem Statement is absolutely key. Very easy to go wrong here, derailing the entire RCCA effort. It is a neutral statement precisely describing what happened and what was the impact. In particular, don’t express the problem in terms of a solution or assumed causes. Problem is NOT “we need to….”
2nd bullet question makes the problem easier for people to relate to and keeps them focused and motivated. Also can help define the scope of the problem (which parts, which assemblies, which customers).
Examples:
  Quality—Customer unplanned downtime, unhappy
  Engineering—Can’t hit our production goals, can’t implement cost reduction goals
  Safety—employee injured on the job (self evidently unacceptable)
With Current Status, this slide serves as a 1 page summary of the issue, keeping everyone aligned. An executive, or a new team member, should be able to look at this slide and get oriented to the issue in 10 seconds.

## Slide 9: Containment (Short Term Band-Aid)
What was the Containment?
What are the risks associated with the Containment?
How do we monitor the situation before implementation of the Corrective Action?
Notes: Containment is a Band-Aid. Immediately addresses the symptoms. Organizations tend to put in place a containment and then forget about the problem, which doesn’t really SOLVE anything. There are also big risks of causing new issues with the containment, and/or having the containment eventually fail.
Examples:
  Quality—immediately ship replacement laser
  Engineering—run extra shifts at reduced speed; buy extra spares to replace the parts that are breaking at higher speed
  Safety—notify everyone to replace any sticky mats that get wet (even if you cleaned up the spill)
Questions on this slide help mitigate risk, while emphasizing the temporary nature of the Containment.
Narrative format of the questions helps step the team through the process, together.

## Slide 10: Root Cause Analysis
What was the Root Cause?
Why should we believe it was the Root Cause?
Notes: This is the core of the process, and where most of the work will be done. Can and should use tools such as Pareto Charts, Fishbone Diagram, 5 Why’s, etc. to find root cause. Need to address the root cause in order to systematically fix the problem and prevent recurrence. This step is the easiest to mess up—people are in a rush, the root cause may seem obvious…but if you get it wrong, you will pay for it later.
(Hint: root cause is almost never “operator error” or similar blame that can be placed on a person. Instead look at procedures, policies, practices, equipment, training, and the like which can be changed to SYSTEMATICALLY address the problem.)
  Cannot overstate the importance of looking for SYSTEM causes rather than people to blame—without this forward looking approach, you will breed a dysfunctional CYA culture, and will never have an honest and objective RCCA investigation. Everyone will be too busy trying to avoid blame.
So the second question is a pre-emptive challenge, reminding the team that there will be a critical public review of their work. They need to be data-driven, and truly demonstrate that they’ve found the root cause.
Advanced topic #1: some theoreticians will tell you there can only be one root cause. That has not been my experience. Regardless, if you find multiple problems that can be considered “root cause”--take the opportunity to fix them all!
Advanced topic #2: during this process, you may find issues that have not yet caused a problem but present a risk of causing future problems. Again, take this opportunity to fix them. This may be termed “Risk Management” (ISO 9001) or “Preventative Action” (ISO 13485).
Examples:
  Quality—board supplier changed a component and didn’t tell us—that component is now prone to failure at high power
  Engineering—delicate parts flexing at high speed and colliding, causing breakage and line down
  Safety—Purchasing got a cheaper brand of sticky mat that loses adhesion to floor when it gets wet

## Slide 11: Corrective Action (Addresses Root Cause Long Term)
What was the Corrective Action?
Why should we believe the same problem will not occur again?
Notes: Corrective action methodically and systematically addresses the root cause. R C C A
Examples:
  Quality—board supplier discontinues use of marginal component; replaces/rework of all boards that used it
  Engineering—modify design of delicate parts to minimize flexing at high speed
  Safety—Purchasing discontinues buying cheaper brand of sticky mat; remaining inventory purged
Advanced topic: In the ISO 9001:2015 standard (Clause 10.2), there is a step required called “effectiveness verification”. That is what the last bullet is calling for—prove the solution put into place actually solved the problem, with objective evidence (data, feedback, etc). If not, then you don’t know if you actually addressed root cause. So don’t close the RCCA until the effectiveness of the Corrective Action is verified.

## Slide 12: Action Item List
Owner | Description | Due Date | Status
Notes: Remember, this RCCA template is used over time and will change as the process is followed. There will be action items associated with performing the RCCA.
This action list is specific to the RCCA, designed for group discussion during meetings. It is likely to be a subset of a larger list kept in Excel format.
RCCA owner + action list drives accountability
Leave the RCCA open until all related actions are closed.

## Slide 13: RCCA Signoff
Name | Position | Approval Signature | Date
 | Technology Manager |  | 
 | Engineering Manager |  | 
 | Production Manager |  | 
 | Quality Manager |  | 
 | Etc. |  | 
Notes: Each company will want to customize the signoff list, which should be as short as is prudent—recommend 3 to 5 key people.
If the person/organization that reported the issue is not intimately involved in the RCCA process, probably want to close the loop with them on the solution, and solicit their feedback, though not necessarily have them “signoff” formally.
After completion, the RCCA PPT should be archived, along with the associated data and other project files, for future reference. RCCA records used for future reference (traceability).

## Slide 14: How will RCCA improve the organization?
RCCA process addresses the root causes of problems, so they don’t recur – minimizes wasteful “fire fighting” crises
RCCA is ideal for groups, effectively harnessing the expertise in the “hive mind”, while avoiding ineffective ego-driven arguments
RCCA builds a company culture of effective problem solving
Implementation of RCCA is an
investment in organizational success
Notes: Every RCCA completed makes the organization stronger, more capable, more robust. It’s a mechanism of continuous improvement for the organization. You want your company to become more capable and more effective over time, with fewer problems, rather than progressively more chaotic and difficult to manage.
Benefits of following this sort of formalized process is not only more efficient and effective problem solving, but building a culture where people think about problems the right way. Eventually they will instinctively run through the RCCA process even for minor problems that they can solve themselves without opening a formal RCCA.

## Slide 15: Summary: This is what you learned
RCCA is a structured problem solving process
RCCA permanently addresses problems that occur
The core slides in this presentation may be used as a template for implementing RCCA
Implementation of RCCA improves your organization’s effectiveness, efficiency, and product quality
Notes: RCCA as structured problem solving process—input=problem, output=solution

## Slide 16: Contact Information
MPIA Website
https://www.montanaphotonics.org/
MPIA Quality Alliance
https://www.montanaphotonics.org/quality-alliance/
Trainers | Company | Role | Email
Ben Klein | FLIR Systems Inc. | Quality Manager | benjamin.klein@teledyneflir.com
Daniel Juliano | MSU Technology Transfer Office | Director | daniel.juliano@montana.edu
Mary Johnson | Wavelength Electronics | CEO | mary@teamwavelength.com
Steve Birrell | Quantum Composers | CEO | sbirrell@quantumcomposers.com
Conlin Ritter | Quantel/Lumibird | Quality Manager | conlin.ritter@gmail.com
Kurt Borge | Quality Time Montana | Quality Consultant | kborge1952@gmail.com
Sara Mines | CACI (formerly AVT) | Quality Director | sara.mines@caci.com